## Slide 1: PHYS 1441 – Section 002 Lecture #10
Wednesday, Oct. 3, 2018
Dr. Jaehoon Yu
Chapter 24 Capacitance etc..
  Capacitors
  Capacitors in Series or Parallel
  Electric Energy Storage
  Effect of Dielectric
  Molecular description of Dielectric Material

## Slide 2: Announcements
Mid Term Exam
  In class Wednesday, Oct. 17
  Covers CH21.1 through what we cover in class Monday, Oct. 15 + appendix
  Bring your calculator but DO NOT input formula into it!
    Cell phones or any types of computers cannot replace a calculator!
  BYOF: You may bring a one 8.5x11.5 sheet (front and back) of handwritten formulae and values of constants
  No derivations, word definitions or solutions of any kind!
  No additional formulae or values of constants will be provided!
Colloquium 4pm today in SH101
  Dr. Xi Zhang of U.C. Santa Cruz

## Slide 4: Capacitors (or Condensers)
What is a capacitor?
  A device that can store electric charge
  But does not let them flow through
What does a capacitor consist of?
  Usually consists of two conducting objects (plates or sheets) placed near each other without touching
  Why can’t they touch each other?
    The charge will neutralize…
Can you give some examples?
  Camera flash, Surge protectors, binary circuits, memory, etc…
How is the capacitor different than the battery?
  Battery provides potential difference by storing energy (usually chemical energy) while the capacitor stores charges but very little energy.

## Slide 5: Capacitors
A simple capacitor consists of a pair of parallel plates of area A separated by a distance d.
  A cylindrical capacitor is essentially parallel plates wrapped around as a cylinder.
How do you draw symbols for a capacitor and a battery in a circuit diagram?
  Capacitor -||-
  Battery (+) -|i- (-)
Circuit
Diagram

## Slide 6: Capacitors
What do you think will happen if a battery is connected ( or the voltage is applied) to a capacitor?
  The capacitor gets charged quickly, one plate positive and the other negative in equal amount.
The battery terminals, the wires and the plates are conductors. What does this mean?
  All conductors are at the same potential. And?
  So the full battery voltage is applied across the capacitor plates.
So for a given capacitor, the amount of charge stored on each capacitor plate is proportional to the potential difference Vba between the plates. How would you write this formula?
  C is a proportionality constant, called the capacitance of the device.
  What is the unit?
C/V
or
Farad (F)
C is the property of a capacitor so does not depend on Q or V.
Normally use μF or pF.

## Slide 7: Determination of Capacitance
C can be determined analytically for a capacitor with a simple geometry and air in between.
Let’s consider a parallel plate capacitor.
  Plates have area A each and separated by d.
    d is smaller than the length, and so E is uniform.
  E for parallel plates is E=σ/ε0, σ=Q/A is the surface charge density.
E and V are related
Since we take the integral from the lower potential (a) to the higher potential (b) along the field line, we obtain
So from the formula:
  What do you notice?
C only depends on the area and the distance of the plates and the permittivity of the medium between them.

## Slide 8: Example 24 – 1
Capacitor calculations: (a) Calculate the capacitance of a capacitor whose plates are 20cmx3.0cm and are separated by a 1.0mm air gap. (b) What is the charge on each plate if the capacitor is connected to a 12-V battery? (c) What is the electric field between the plates? (d) Estimate the area of the plates needed to achieve a capacitance of 1F, given the same air gap.
(a) Using the formula for a parallel plate capacitor, we obtain
(b) From Q=CV, the charge on each plate is

## Slide 9: Example 24 – 1
(C) Using the formula for the electric field in two parallel plates
(d) Solving the capacitance formula for A, we obtain
Or, since
we can obtain
Solve for A
About 40% the area of Arlington (256km2).

## Slide 10: Example 24 – 3
Spherical capacitor: A spherical capacitor consists of two thin concentric spherical conducting shells, of radius ra and rb, as in the figure. The inner shell carries a uniformly distributed charge Q on its surface and the outer shell an equal but opposite charge –Q. Determine the capacitance of the two shells.
Using Gauss’ law, the electric field outside a uniformly charged conducting sphere is
So the potential difference between a and b is
Thus capacitance is

## Slide 11: Capacitor Cont’d
A single isolated conductor can be said to have a capacitance, C.
C can still be defined as the ratio of the charge to the absolute potential V on the conductor.
  So Q=CV.
The potential of a single conducting sphere of radius rb can be obtained as
So its capacitance is
where

## Slide 12: Capacitors in Series or Parallel
Capacitors may be used in electric circuits
What is an electric circuit?
  A closed path of conductors, usually wires connecting capacitors and other electrical devices, in which
    charges can flow
    And includes a voltage source such as a battery
Capacitors can be connected in various ways.
  In parallel, in series or in combination

## Slide 13: Capacitors in Parallel
Parallel arrangement provides the same voltage across all the capacitors.
  Left hand plates are at Va and right hand plates are at Vb
  So each capacitor plate acquires charges given by the formula
    Q1=C1V, Q2=C2V, and Q3=C3V
The total charge Q that must leave the battery is then
  Q=Q1+Q2+Q3=V(C1+C2+C3)
Consider that the three capacitors behave like an equivalent one
  Q=CeqV= V(C1+C2+C3)
Thus the equivalent capacitance in parallel is
What is the net effect?
The capacitance increases!!!

## Slide 14: Capacitors in Series
Series arrangement is more interesting
  When battery is connected, +Q flows to the left plate of C1 and –Q flows to the right plate of C3.
  Since capacitors in between were originally neutral, charges get induced to neutralize the ones in the middle.
  So the charge on each capacitor plate is the same value, Q. (Same charge)
Consider that the three capacitors behave like an equivalent one
  Q=CeqV
The total voltage V across the three capacitors in series must be equal to the sum of the voltages across each capacitor.
  V=V1+V2+V3=Q/C1+Q/C2+Q/C3
Putting all these together, we obtain:
V=Q/Ceq=Q(1/C1+1/C2+1/C3)
Thus the equivalent capacitance is
What is the net effect?
The capacitance smaller than the smallest C!!!

## Slide 15: Example 24 – 5
Equivalent Capacitor: Determine the capacitance of a single capacitor that will have the same effect as the combination shown in the figure. Take C1=C2=C3=C.
We should do these first!!
Now the equivalent capacitor is in series with C1.
How?
These are in parallel so the equivalent capacitance is:
Solve for Ceq

## Slide 16: Electric Energy Storage
A charged capacitor stores energy.
  The stored energy is the amount of the work done to charge it.
The net effect of charging a capacitor is removing one type of charge from one plate and put them on to the other.
  Battery does this when it is connected to a capacitor.
Capacitors do not get charged immediately.
  Initially when the capacitor is uncharged, no work is necessary to move the first bit of charge. Why?
    Since there is no charge, there is no field that the external work needs to overcome.
  When some charge is on each plate, it requires work to add more charges of the same sign due to the electric repulsion.

## Slide 17: Electric Energy Storage
The work needed to add a small amount of charge, dq, when a potential difference across the plate is V: dW=Vdq.
Since V=q/C, the work needed to store total charge Q is
Thus, the energy stored in a capacitor when the capacitor carries the charges +Q and –Q is
Since Q=CV, we can rewrite

## Slide 18: Example 24 – 8
Energy store in a capacitor: A camera flash unit stores energy in a 150mF capacitor at 200V. How much electric energy can be stored?
So we use the one with C and V:
Umm.. Which one?
Using the formula for stored energy.
What do we know from the problem?
C and V
How do we get J from FV2?

## Slide 19: Electric Energy Density
The energy stored in a capacitor can be considered as being stored in the electric field between the two plates
For a uniform field E between two plates, V=Ed and C=ε0A/d
Thus the stored energy is
Since Ad is the gap volume V, we can obtain the energy density, stored energy per unit volume, as
Electric energy stored per unit volume in any region of space is proportional to the square of E in that region.
Valid for any space that is vacuum

## Slide 20: Dielectrics
Capacitors have an insulating sheet of material, called dielectric, between the plates to
  Increase breakdown voltage greater than that in air (3MV/m)
  Apply higher voltage to the gap without the charge passing across
  Allow the plates get closer together without touching
    Increases capacitance ( recall C=ε0A/d)
  Increase the capacitance by the dielectric constant
  Where C0 is the intrinsic capacitance when the gap is vacuum

## Slide 21: Dielectrics
The value of dielectric constant K varies depending on the material (Table 24 – 1)
  K for vacuum is 1.0000
  K for air is 1.0006 (this is why permittivity of air and vacuum are used interchangeably.)
  K for paper is 3.7
Maximum electric field before breakdown occurs is called the dielectric strength. What is its unit?
  V/m
The capacitance of a parallel plate capacitor with a dielectric (K) filling the gap is

## Slide 22: Dielectrics
A new quantity of the permittivity of a dielectric material is defined as ε=Kε0
The capacitance of a parallel plate capacitor with a dielectric medium filling the gap is
The energy density stored in an electric field E in a dielectric is
Valid for any space w/ dielectric w/ permittivity ε.
What is the stored energy in between ProtoDUNE cathode (-600kV) plate (6mx6m) and the cryostat wall (0V), d=1.5m, LAr K=1.6?

## Slide 23
Field Cage and cathode hangs off of the ceiling
Essential to have light yet sturdy structure
Based on modular concept as SP
ProtoDUNE Dual Phase
Charge Readout Planes
Field Cage (common structural elements with SP)
Cathode
6 m
6 m
1.5 m

## Slide 24
DUNE Dual Phase
Cathode

## Slide 25: Effect of a Dielectric Material on Capacitance
Let’s consider the two cases below:
Constant voltage: Experimentally observed that the total charge on the each plate of the capacitor increases by K as a dielectric material is inserted between the gap  Q=KQ0
  The capacitance increased to C=Q/V0=KQ0/V0=KC0
Constant charge: Voltage found to drop by a factor K  V=V0/K
  The capacitance increased to C=Q0/V=KQ0/V0=KC0
Case #1 : constant V
Case #2 : constant Q

## Slide 26: Effect of a Dielectric Material on Field
What happens to the electric field within a dielectric?
Without a dielectric, the field is
  What are V0 and d?
    V0: Potential difference between the two plates
    d: separation between the two plates
For the constant voltage, the electric field remains the same
For the constant charge: the voltage drops to V=V0/K, thus the field in the dielectric is
  The field in the dielectric is reduced.

## Slide 27: Example 24 – 11
Dielectric Removal: A parallel-plate capacitor, filled with the dielectric of K=3.4, is connected to a 100-V battery. After the capacitor is fully charged, the battery is disconnected. The plates have area A=4.0m2, and are separated by d=4.0mm. (a) Find the capacitance, the charge on the capacitor, the electric field strength, and the energy stored in the capacitor. (b) The dielectric is carefully removed, without changing the plate separation nor does any charge leave the capacitor. Find the new value of capacitance, electric field strength, voltage between the plates and the energy stored in the capacitor.
(a)

## Slide 28: Example 24 – 11 cont’d
Since charge is the same ( ) before and after the removal of the dielectric, we obtain
(b)
Since the dielectric has been removed, the effect of dielectric constant must be removed as well.
Where did the extra energy come from?
The energy conservation law is violated in electricity???
An external force has done the work of 3.6x10-4J on the system to remove dielectric!!
Wrong!
Wrong!
Wrong!

## Slide 29: Molecular Description of Dielectric
So what in the world makes dielectrics behave the way they do?
We need to examine this in a microscopic scale.
Let’s consider a parallel plate capacitor that is charged up +Q(=C0V0) and –Q with air in between.
  Assume there is no way any charge can flow in or out
Now insert a dielectric
  Dielectric can be polar  could have permanent dipole moment. What will happen?
Due to the electric field molecules will be aligned.

## Slide 30: Molecular Description of Dielectric
OK. Then what happens?
Then effectively, there will be some negative charges close to the surface of the positive plate and positive charge on the negative plate
  Some electric field do not pass through the whole dielectric but stops at the negative charge
  So the field inside dielectric is smaller than the air
Since electric field is smaller, the force is smaller
  The work need to move a test charge inside the dielectric is smaller
  Thus the potential difference across the dielectric is smaller than across the air

## Slide 31: Electric Current and Resistance
So far we have been studying static electricity
  What is the static electricity?
    The charges so far has not been moving but staying put at the location they are placed.
Now we will learn dynamics of electricity
What is the electric current?
  A flow of electric charge
  A few examples of the things that use electric current in everyday lives?
In an electrostatic situation, there is no electric field inside a conductor but when there is current, there is field inside a conductor. Why?
  Electric field is needed to keep charges moving

## Slide 32: The Electric Battery
What is a battery?
  A device that produces electrical energy from the stored chemical energy and produces electricity  Maintains potential difference!
Electric battery was invented by Volta in 1790s in Italy
  It was made of disks of zinc and silver based on his research that certain combinations of materials produce a greater electromotive force (emf), or potential, than others
Simplest batteries contain two plates made of dissimilar metals called electrodes
  Electrodes are immersed in a solution, the electrolyte
  This unit is called a cell and many of these form a battery
Zinc and Iron in the figure are called terminals

## Slide 33: How does a battery work?
One of the electrodes in the figure is zinc and the other carbon
The acid electrolyte reacts with the zinc electrode and dissolves it.
Each zinc atom leaves two electrons in the electrode and enters into the solution as a positive ion  zinc electrode acquires negative charge and the electrolyte (the solution) becomes positively charged
The carbon electrode picks up the positive charge
Since the two terminals are oppositely charged, there is a potential difference between them

## Slide 34: How does a battery work?
When the terminals are not connected, only the necessary amount of zinc is dissolved into the solution.
How is a particular potential maintained?
  If the terminals are not connected, as too many of zinc ion gets produced,
    zinc electrode gets increasingly charged up negative
    zinc ions get recombined with the electrons in zinc electrode
Why does battery go dead?
  When the terminals are connected, the negative charges will flow away from the zinc electrode
  More zinc atoms dissolve into the electrolyte to produce more charge
  One or more electrode get used up not producing any more charge.

## Slide 35: Electric Current
When a circuit is powered by a battery (or a source of emf) the charge can flow through the circuit.
Electric Current: Any flow of charge
  Current can flow whenever there is a potential difference between the ends of a conductor (or when the two ends have opposite charges)
    The current can flow even through the empty space under certain conditions
  Electric current in a wire can be defined as the net amount of charge that passes through the wire’s full cross section at any point per unit time (just like the flow of water through a conduit.)
  Average current is defined as:
  The instantaneous current is:
  What kind of a quantity is the current?
Unit of the current?
C/s
1A=1C/s
In a single circuit, conservation of electric charge guarantees that the current at one point of the circuit is the same as any other points on the circuit.
Scalar

## Slide 36: Example 25 – 1
Current is a flow of charge: A steady current of 2.5A flows in a wire for 4.0min. (a) How much charge passed by any point in the circuit? (b) How many electrons would this be?
Current is total amount charge flown through a circuit in a given time. So from we obtain
The total number of electrons passed through the circuit is