## Slide 1: PHYS 1441 – Section 002 Lecture #20
Monday, Nov. 26, 2018
Dr. Jaehoon Yu
Chapter 29:EM Induction & Faraday’s Law
  Lenz’s Law
  Generation of Electricity
  Transformer
  Electric Field Due to Changing Magnetic Flux
Chapter 30: Inductance
  Inductance
  Mutual and Self Inductance

## Slide 2: Announcements – I
Class feedback review ongoing!
  We will do this in class this Wednesday, Nov. 28 after the quiz. So please bring your devices
Quiz 3 results
  Class average: 40/55  equivalent to 72.4/100
    Previous quizzes: 74/100 and 55/100
  Top score: 55/55
Term 2 results
  Class average: 73/96  equivalent to 76/100
    Previous exams: 61/100 and 71/100
  Top score: 90/96

## Slide 3: Announcements – II
Quiz #4
  Beginning of the class this Wednesday, Nov. 28
  Covers: CH28.6 – what we finish today, Nov. 26
  Bring your calculator but DO NOT input formula into it!
    Cell phones or any types of computers cannot replace a calculator!
  BYOF: You may bring a one 8.5x11.5 sheet (front and back) of handwritten formulae and values of constants
  No derivations, word definitions or solutions of any kind!
  No additional formulae or values of constants will be provided!
Final comprehensive exam
  In class 1:00 – 2:20pm, Wed. Dec. 5
  Covers CH21.1 through what we finish next Monday, Dec. 3
  BYOF

## Slide 4: Reminder: Special Project #5
Make a list of the power consumption and the resistance of all electric and electronic devices at your home and compile them in a table. (10 points total for the first 10 items and 0.5 points each additional item.)
Estimate the cost of electricity for each of the items on the table using your own electric cost per kWh (if you don’t find your own, use $0.12/kWh) and put them in the relevant column. (5 points total for the first 10 items and 0.2 points each additional items)
Estimate the the total amount of energy in Joules and the total electricity cost per day, per month and per year for your home. (8 points)
Spreadsheet can be downloaded from the class web page: http://www-hep.uta.edu/~yu/teaching/fall18-1444-002/fall18-1444-002.html
Due: Beginning of the class this Wednesday, Nov. 28

## Slide 5: Example 29 – 5
Pulling a coil from a magnetic field. A square coil of wire with side 5.00cm contains 100 loops and is positioned perpendicular to a uniform 0.600-T magnetic field. It is quickly and uniformly pulled from the field (moving perpendicular to B) to a region where B drops abruptly to zero. At t=0, the right edge of the coil is at the edge of the field. It takes 0.100s for the whole coil to reach the field-free
What should be computed first?
The flux at t=0 is
The change of flux is
region. Find (a) the rate of change in flux through the coil, (b) the emf and the current induced, and (c) how much energy is dissipated in the coil if its resistance is 100Ω. (d) what was the average force required?
The initial flux at t=0.
Thus the rate of change of the flux is

## Slide 6: Example 29 – 5, cnt’d
Thus the total emf induced in this period is
Which direction would the induced current flow?
The total energy dissipated is
Force for each coil is
The induced current in this period is
Clockwise
Force for N coil is

## Slide 7: EMF Induced on a Moving Conductor
Another way of inducing emf is using a U shaped conductor with a movable rod resting on it.
As the rod moves at speed v, it travels vdt in time dt, changing the area of the loop by dA=lvdt.
Using Faraday’s law, the induced emf for this loop is
  This equation is valid as long as B, l and v are perpendicular to each other. What do we do if not?
    Use the scalar product of the vector quantities
An emf induced on a conductor moving in a magnetic field is called a motional emf

## Slide 8: Electric Generators
What does a generator do?
  Transforms mechanical energy into electrical energy
  What does this look like?
    An inverse of an electric motor which transforms electrical energy to mechanical energy
  An electric generator is also called a dynamo
Whose law does the generator based on?
  Faraday’s law of induction

## Slide 9: How does an Electric Generator work?
An electric generator consists of
  Many coils of wires wound on an armature that can rotate by mechanical means in a magnetic field
An emf is induced in the rotating coil
Electric current is the output of a generator
Which direction does the output current flow when the armature rotates counterclockwise?
  The conventional current flows outward on wire A toward the brush
  After half the revolution the wire A will be where the wire C is and the current flow on A is reversed
Thus the current produced is alternating its direction

## Slide 10: How does an Electric Generator work?
Let’s assume the loop is rotating in a uniform B field w/ a constant angular velocity ω. The induced emf is
What is the variable that changes above?
  The angle θ. What is dθ/dt?
    The angular speed ω.
  So θ=θ0+ωt
  If we choose θ0=0, we obtain
  If the coil contains N loops:
  What is the shape of the output?
    Sinusoidal w/ an amplitude ε0=NBAω
USA frequency is 60Hz. Europe is at 50Hz
  Most the U.S. power is generated at steam plants

## Slide 11: Example 29 – 9
An AC generator. The armature of a 60-Hz AC generator rotates in a 0.15-T magnetic field. If the area of the coil is 2.0x10-2m2, how many loops must the coil contain if the peak output is to be ε0=170V?
The maximum emf of a generator is
Solving for N
Since
We obtain

## Slide 12: US Electricity Sources

## Slide 13: US Electric E Consumption by Users
US Energy Information Administration http://www.eia.gov/electricity/

## Slide 14: The World Energy Consumption
In 2013, total worldwide energy consumption was 567 EJ (567×1018 J=157 PWh) expected >1000EJ by 2050
  Equivalent to an average energy consumption rate of 18 terawatts (1.8×1013 W)
  US uses 39.1 PWh (1.38kWh/person, as of 2014)
The potential for renewable energy
  solar energy 1600 EJ (444,000 TWh)
  wind power 600 EJ (167,000 TWh)
  geothermal energy 500 EJ (139,000 TWh),
  biomass 250 EJ (70,000 TWh)
  hydropower 50 EJ (14,000 TWh) an
  ocean energy 1 EJ (280 TWh)
  Read this paper if you want to learn more

## Slide 15: A DC Generator
A DC generator is almost the same as an AC generator except the slip rings are replaced by split-ring commutators
Output can be smoothed out by placing a capacitor in parallel to the output
  More commonly done using many armature windings
Smooth output using many windings

## Slide 16: Transformer
What is a transformer?
  A device for increasing or decreasing an AC voltage
  A few examples?
    TV sets to provide the high voltage to picture tubes, portable electronic device converters, transformers on the pole, etc
A transformer consists of two coils of wires known as the primary and the secondary
  The two coils can be interwoven or linked by a laminated soft iron core to reduce losses due to Eddy current
Transformers are designed so that all magnetic flux produced by the primary coil pass through the secondary

## Slide 17: How does a transformer work?
When an AC voltage is applied to the primary, the changing B it produces will induce voltage of the same frequency in the secondary wire
So how would we make the voltage different?
  By varying the number of loops in each coil
  From Faraday’s law, the induced emf in the secondary is
  The input primary voltage is
  Since dΦB/dt is the same, we obtain
Transformer Equation

## Slide 18: Transformer Equation
The transformer equation does not work for DC current
  Since there is no change of magnetic flux!!
If NS>NP, the output voltage is greater than the input so it is called a step-up transformer while NS<NP is called step-down transformer
Now, it looks like energy conservation is violated since we can get more emf from smaller ones, right?
  Wrong! Wrong! Wrong! Energy is always conserved!
  A well designed transformer can be more than 99% efficient
  The power output is the same as the input:
The output current for a step-up transformer will be lower than the input, while it is larger for a step-down x-former than the input.

## Slide 19: Example for A Transformer
Portable radio transformer. A transformer for home use of a portable radio reduces 120-V AC to 9.0V AC. The secondary contains 30 turns, and the radio draws 400mA. Calculate (a) the number of turns in the primary (b) the current in the primary and (c) the power transformed.
(a) What kind of a transformer is this?
A step-down x-former
Since
We obtain
(b) Also from the transformer equation
We obtain
(c) Thus the power transformed is
How about the input power?
The same assuming 100% efficiency.

## Slide 20: Example 29 – 13: Power Transmission
Transmission lines. An average of 120kW of electric power is sent to a small town from a power plant 10km away. The transmission lines have a total resistance of 0.4Ω. Calculate the power loss if the power is transmitted at (a) 240V and (b) 24,000V.
We cannot use P=V2/R since we do not know the voltage along the transmission line. We, however, can use P=I2R.
(a) If 120kW is sent at 240V, the total current is
Thus the power loss due to transmission line is
(b) If 120kW is sent at 24,000V, the total current is
Thus the power loss due to transmission line is
The higher the transmission voltage, the smaller the current, causing less loss of energy. This is why power is transmitted w/ HV, as high as 170kV.

## Slide 21: Electric Field due to Magnetic Flux Change
When the electric current flows through a wire, there is an electric field in the wire that moves electrons
We saw, however, that changing magnetic flux induces a current in the wire. What does this mean?
  There must be an electric field induced by the changing magnetic flux.
In other words, a changing magnetic flux produces an electric field
This result applies not just to wires but to any conductor or any region in space

## Slide 22: Generalized Form of Faraday’s Law
Recall the relationship between the electric field and the potential difference
Induced emf in a circuit is equal to the work done per unit charge by the electric field
So we obtain
The integral is taken around a path enclosing the area through which the magnetic flux ΦB is changing.