## Slide 1: PHYS 1444 – Section 002 Lecture 15
Monday, Oct. 21, 2019
Dr. Jaehoon Yu
CH 26
  EMF and Terminal Voltage
  Resistors in Series and Parallel
  Kirchhoff’s rules
  RC Circuit
CH 27: Magnetism & Magnetic Field
  Electric Current and Magnetism
Today’s homework is #9, due 11pm, Wednesday, Oct. 31!!

## Slide 2: Announcements
Mid-term grade discussions
  From 12:00 – 2:30pm, this Wednesday, Oct. 23 in my office (CPB342)
  Last name starts with A – D (12 – 12:30), E– K (12:30 – 1), L – O (1 – 1:30), P – S (1:30 – 2:00), T – Z (2-2:30)
Mid-term exam results
  Class average: 76.1/104
    Equivalent to : 73.2/100
    Previous exam: 51.2/100
  Top score: 100/104
Remember the triple extra credit colloquia
  Wed. Oct. 30: Prof. Liangtao Wang of U. of Chicago
  Wed. Nov. 13: Prof Hitoshi Murayama of U.C. Berkeley

## Slide 3: Special Project #5
Make a list of the power consumption and the resistance of all electric and electronic devices at your home and compile them in a table. (10 points total for the first 10 items and 0.5 points each additional item.)
Estimate the cost of electricity for each of the items on the table using your own electric cost per kWh (if you don’t find your own, use $0.12/kWh) and put them in the relevant column. (5 points total for the first 10 items and 0.2 points each additional items)
Estimate the the total amount of energy in Joules and the total electricity cost per day, per month and per year for your home. (8 points)
Due: Beginning of the class Monday, Nov. 11

## Slide 5: EMF and Terminal Voltage
What do we need to have a current in an electric circuit?
  A device that provides a potential difference, such as a battery or a generator
    They normally convert some types of energy into the electric energy
    These devices are called source of electromotive force (emf)
      This is does NOT refer to a real “force”.
Potential difference between terminals of an emf source, when no current flows to an external circuit, is called the emf (E) of the source.
The battery itself, however, has some internal resistance (r) due to the flow of charges in the electrolyte
  Why does the headlight dim when you start the car?
    The starter needs a large amount of current but the battery cannot provide charge fast enough to supply current to both the starter and the headlight

## Slide 6: EMF and Terminal Voltage
Since the internal resistance is inside the battery, we can never separate them out.
So the terminal voltage difference is Vab=Va-Vb.
When no current is drawn from the battery, the terminal voltage equals the emf which is determined by the chemical reaction; Vab= E.
However when the current I flows naturally from the battery, there is an internal drop in voltage which is equal to Ir. Thus the actual delivered terminal voltage to the circuit is

## Slide 7: Resistors in Series
Resistors are in series when two or more resistors are connected end to end
  These resistors represent simple resistors in circuit or electrical devices, such as light bulbs, heaters, dryers, etc
What is common for devices in a series circuit?
  Current is the same through all the elements in series
Potential difference across every element in the circuit is
  V1=IR1, V2=IR2 and V3=IR3
Since the total potential difference is V, we obtain
  V=IReq=V1+V2+V3=I(R1+R2+R3)
  Thus, Req=R1+R2+R3
Resistors in series
When resistors are connected in series, the total resistance increases and the current decreases.

## Slide 8: Energy Losses in Resistors
Why is it true that V=V1+V2+V3?
What is the potential energy loss when charge q passes through resistors R1, R2 and R3
  ΔU1=qV1, ΔU2=qV2, ΔU3=qV3
Since the total energy loss should be the same as the total energy provided to the system, we obtain
  ΔU=qV=ΔU1+ΔU2+ΔU3=q(V1+V2+V3)
  Thus, V=V1+V2+V3

## Slide 9: Example 26 – 1
Battery with internal resistance. A 65.0-Ω resistor is connected to the terminals of a battery whose emf is 12.0V and whose internal resistance is 0.5-Ω. Calculate (a) the current in the circuit, (b) the terminal voltage of the battery, Vab, and (c) the power dissipated in the resistor R and in the battery’s internal resistor.
(a) Since
We obtain
Solve for I
(b) The terminal voltage Vab is
(c) The power dissipated in R and r are
What is this?
A battery or a source of emf.

## Slide 10: Resistors in Parallel
What is common for the devices in a parallel circuit?
  The voltage is the same across all the resistors in the same circuit
  The total current that leaves the battery is, however, split.
The current that passes through every element is
  I1=V/R1, I2=V/R2, I3=V/R3
Since the total current is I, we obtain
  I=V/Req=I1+I2+I3=V(1/R1+1/R2+1/R3)
  Thus, 1/Req=1/R1+1/R2+1/R3
Resistors in parallel
When resistors are connected in parallel, the total resistance decreases and the current increases.
Resistors are in parallel when two or more resistors are connected in separate branches
  Most the house and building wirings are arranged this way.

## Slide 11: Resister and Capacitor Arrangements
Parallel Capacitor arrangements
Parallel Resistor arrangements
Series Capacitor arrangements
Series Resistor arrangements

## Slide 12: Example 26 – 2
Series or parallel? (a) The light bulbs in the figure are identical and have identical resistance R. Which configuration produces more light? (b) Which way do you think the headlights of a car are wired?
(a) What are the equivalent resistances for the two cases?
Series
The bulbs get brighter when the total power transformed is larger.
series
Parallel
So
parallel
So parallel circuit provides brighter lighting.
(b) Car’s headlights are in parallel to provide brighter lighting and also to prevent both lights going out at the same time when one burns out.
So what is bad about parallel circuits?
Uses more energy in a given time.

## Slide 13: Example 26 – 5
Current in one branch. What is the current flowing through the 500-Ω resistor in the figure?
What do we need to find first?
Thus the total current in the circuit is
We need to find the total current.
To do that we need to compute the equivalent resistance.
Req of the small parallel branch is:
Req of the circuit is:
The voltage drop across the parallel branch is
The current flowing across 500-Ω resistor is therefore
What is the current flowing 700-Ω resister?

## Slide 14: Kirchhoff’s Rules – 1st Rule
Some circuits are very complicated to do the analysis using simple combinations of resisters
  G. R. Kirchhoff devised two rules to deal with complicated circuits.
Kirchhoff’s rules are based on conservation of charge and conservation of energy
  Kirchhoff’s 1st rule: The junction rule, charge conservation.
    At any junction point, the sum of all currents entering the junction must be equal to the sum of all currents leaving the junction.
    In other words, what goes in must come out.
    At junction a in the figure, I3 comes into the junction while I1 and I2 leaves: I3 = I1+ I2

## Slide 15: Kirchhoff’s Rules – 2nd Rule
Kirchoff’s 2nd rule: The loop rule, uses conservation of energy.
  The sum of the changes in potential in any closed path of a circuit must be zero.
The current in the circuit in the figure is
  Point e is the high potential point while point d is the lowest potential.
  When the test charge starts at e and returns to e, the total potential change is 0.
  Between point e and a, no potential change since there is no source of potential nor any resistance.
  Between a and b, there is a 400Ω resistance, causing IR=0.017*400 =6.8V drop.
  Between b and c, there is a 290Ω resistance, causing IR=0.017*290 =5.2V drop.
  Since these are voltage drops, we use negative sign for these, -6.8V and -5.2V.
  No change between c and d while from d to e there is +12V change.
  Thus the total change of the voltage through the loop is: -6.8V-5.2V+12V=0V.
I=12/690=0.017A.