## Slide 1: PHYS 1442 – Section 001 Lecture #9
Tuesday, June 18, 2013
Dr. Jaehoon Yu
Chapter 19
  Kirchhoff’s Rules
  EMFs in Series and Parallel
  Capacitors in Series and Parallel
  RC Circuit
Chapter 20
  Magnets and Magnetic Field
  Electric Current and Magnetism
  Magnetic Forces on Electric Current
Today’s homework is homework #5, due 11pm, Monday, June 24!!

## Slide 2: Announcements
Quiz results
  Class average: 58.1/95
    Equivalent to 61.2/100
      Previous result 51.7/100
  Top score: 87/95
Mid-term exam
  Tomorrow, Wednesday, June 19
  Comprehensive exam
    Covers CH16.1 – what we finish today (CH20.1?) plus Appendices A1 – A8
Mid-term grade discussion
  Between 2 – 3:30 pm this Friday, June 21
  In Dr. Yu’s office (CPB342)

## Slide 3: Special Project #3
Make a list of the power consumption and the resistance of all electric and electronic devices at your home and compiled them in a table. (5 points total for the first 10 items and 0.25 points each additional item.)
Estimate the cost of electricity for each of the items on the table using your own electric cost per kWh (if you don’t find your own, use $0.12/kWh) and put them in the relevant column. (2 points total for the first 10 items and 0.1 points each additional items)
Estimate the the total amount of energy in Joules and the total electricity cost per day, per month and per year for your home. (6 points)
Due: Beginning of the class Thursday, June 20
  Print the entire width of the table to be contained in one page!!

## Slide 4: Spread Sheet

## Slide 5: Kirchhoff’s Rules – 1st Rule
Some circuits are very complicated to analyze using the simple combinations of resisters
  G. R. Kirchhoff devised two rules to deal with complicated circuits.
Kirchhoff’s rules are based on conservation of charge and energy
  Kirchhoff’s 1st rule: Junction rule, charge conservation.
    At any junction point, the sum of all currents entering the junction must equal to the sum of all currents leaving the junction.
    In other words, what goes in must come out.
    At junction a in the figure, I3 comes into the junction while I1 and I2 leaves: I3 = I1+ I2

## Slide 6: Kirchhoff’s Rules – 2nd Rule
Kirchoff’s 2nd rule: Loop rule, uses conservation of energy.
  The sum of the changes in potential around any closed path of a circuit must be zero.
The current in the circuit in the figure is I=12/690=0.017A.
  Point e is the highest potential point while point d is the lowest potential.
  When the test charge starts at e and returns to e, the total potential change is 0.
  Between point e and a, no potential change since there is no source of potential or any resistance to drop potential.
  Between a and b, there is a 400Ω resistance, causing IR=0.017*400 =6.8V drop.
  Between b and c, there is a 290Ω resistance, causing IR=0.017*290 =5.2V drop.
  Since these are voltage drops, we use negative sign for these, -6.8V and -5.2V.
  No change between c and d while from d to e there is +12V change.
  Thus the total change of the voltage through the loop is: -6.8V-5.2V+12V=0V.

## Slide 7: Using Kirchhoff’s Rules
Determine the flow of currents at the junctions.
  It does not matter which direction of the current you choose.
  If the value of the current after completing the calculations are negative, you just flip the direction of the current flow.
Write down the current equation based on Kirchhoff’s 1st rule at various junctions.
  Be sure to see if any of them are the same.
Choose independent closed loops in the circuit
Write down the potential in each interval of the junctions, keeping the signs properly.
Write down the potential equations for each loop.
Solve the equations for unknowns.

## Slide 8: Example 19 – 8
Using Kirchhoff’s rules. Calculate the currents I1, I2 and I3 in each of the branches of the circuit in the figure.
The directions of the current through the circuit is not known a priori but since the current tends to move away from the positive terminal of a battery, we arbitrarily choose the direction of the currents as shown.
This is the same for junction d as well, so no additional information.
We have three unknowns so we need three equations.
Using Kirchhoff’s junction rule at point a, we obtain
Now the second rule on the loop ahdcba.
The total voltage change in loop ahdcba is.

## Slide 9: Example 19 – 8, cnt’d
So the three equations become
Now the second rule on the other loop agfedcba.
The total voltage change in loop agfedcba is.
We can obtain the three current by solving these equations for I1, I2 and I3.

## Slide 10: EMF’s in Series and Parallel: Charging a Battery
When two or more sources of emf’s, such as batteries, are connected in series
  The total voltage is the algebraic sum of their voltages, if their direction is the same
    Vac=1.5 + 1.5=3.0V in figure (a).
  If the batteries are arranged in an opposite direction, the total voltage is the difference between them
    Vac=20 – 12=8.0V in figure (b)
    Connecting batteries in opposite direction is wasteful.
    This, however, is the way a battery charger works.
    Since the 20V battery is at a higher voltage, it forces charges into 12V battery
    Some battery are rechargeable since their chemical reactions are reversible but most the batteries can not reverse their chemical reactions
Parallel arrangements (c) are used only to increase currents.
This is the way we jump start a car

## Slide 11: Capacitors in Series or Parallel
Capacitors are also used in many electric circuits.
So what is an electric circuit again?
  A closed path of conductors, usually wires, connecting capacitors, resisters and other electrical devices, in which
    charges can flow
    And includes a source of potential such as a battery
Capacitors can be connected in various ways.
  In parallel and in Series or in combination

## Slide 12: Capacitors in Parallel
Parallel arrangement provides the same voltage across all the capacitors.
  Left hand plates are at Va and right hand plates are at Vb
  So each capacitor plate acquires charges given by the formula
    Q1=C1V, Q2=C2V, and Q3=C3V
The total charge Q that must leave the battery is then
  Q=Q1+Q2+Q3=V(C1+C2+C3)
Consider that the three capacitors behave like an equivalent one
  Q=CeqV= V(C1+C2+C3)
Thus the equivalent capacitance in parallel is
What is the net effect?
The capacitance increases!!!

## Slide 13: Capacitors in Series
Series arrangement is more interesting
  When a battery is connected, +Q flows to the left plate of C1 and –Q flows to the right plate of C3 inducing opposite sign charges on the other plates.
  Since the capacitor in the middle was originally neutral, charges get induced to neutralize the induced charges
  So the charge on each capacitor is the same value, Q. (Same charge)
Consider that the three capacitors behave like an equivalent one
  Q=CeqV  V=Q/Ceq
The total voltage V across the three capacitors in series must be equal to the sum of the voltages across each capacitor.
  V=V1+V2+V3=(Q/C1+Q/C2+Q/C3)
Putting all these together, we obtain:
V=Q/Ceq=Q(1/C1+1/C2+1/C3)
Thus the equivalent capacitance is
What is the net effect?
The capacitance smaller than the smallest C!!!

## Slide 14: Example 19 – 10
Equivalent Capacitor: Determine the capacitance of a single capacitor that will have the same effect as the combination shown in the figure. Assume C1=C2=C3=C.
We should do these first!!
Now the equivalent capacitor is in series with C1.
How?
These are in parallel so the equivalent capacitance is:
Solve for Ceq

## Slide 15: Resister and Capacitor Arrangements
Parallel Capacitor arrangements
Parallel Resister arrangements
Series Capacitor arrangements
Series Resister arrangements

## Slide 16: RC Circuits
Circuits containing both resisters and capacitors
  RC circuits are used commonly in everyday life
    Control windshield wiper
    Timing of traffic light color change
    Camera flashes and heart pacemakers
How does an RC circuit look?
  There should be a source of emf, capacitors and resisters
What happens when the switch S is closed?
  Current immediately starts flowing through the circuit.
  Electrons flows out of negative terminal of the emf source, through the resister R and accumulates on the upper plate of the capacitor
  The electrons from the bottom plate of the capacitor flow into the positive terminal of the battery, leaving only positive charge on the bottom plate
  As the charge accumulates on the capacitor, the potential difference across it increases
  The current reduces gradually to 0 until the voltage across the capacitor is the same as emf.
  The charge on the capacitor increases unil it reaches to its maximum, Cε.
  What happens when the battery in the circuit is replaced with a wire?
Capacitor discharges

## Slide 17: RC Circuits
How does all this look like in graphs?
  Charge and the current on the capacitor as a function of time
  From energy conservation (Kirchhoff’s 2nd rule), the emf ε must be equal to the voltage drop across the capacitor and the resister
    ε=IR+Q/C
    R includes all resistance in the circuit, including the internal resistance of the battery, I is the current in the circuit at any instant, and Q is the charge of the capacitor at that same instance.

## Slide 18: Analysis of RC Circuits
Charge and voltage
What can we see from the above equations?
  Q and VC increase from 0 at t=0 to maximum value Qmax=Cε and VC= ε.
In how much time?
  The quantity RC is called the time constant, τ, of the circuit
    τ=RC, What is the unit?
  What is the physical meaning?
    The time required for the capacitor to reach (1-e-1)=0.63 or 63% of its full charge
The current is
Sec.

## Slide 19: Discharging RC Circuits
  The rate at which the charge leaves the capacitor equals the negative of the current flows through the resistor
    I= - ΔQ/Δt. Why negative?
    Since the current is leaving the capacitor
  Thus the voltage equation becomes a differential equation
When a capacitor is already charged, it is allowed to discharge through a resistance R.
  When the switch S is closed, the voltage across the resistor at any instant equals that across the capacitor. Thus IR=Q/C.
Rearrange terms

## Slide 20: Discharging RC Circuits
  What happens when an RC circuit discharges from its original charge of Q0?
  Charge at any given time t is
  What does this tell you about the charge on the capacitor?
    It decreases exponentially with time at a time constant RC
    Just like the case of charging
  The current is:
  The voltage is:

## Slide 21: Ex. 19 – 12
Discharging RC circuit. If a charged capacitor C=35μF is connected to a resistance R=120Ω as in the figure, how much time will elapse until the voltage falls to 10% of its original (maximum) value?
Since we are looking for the time it takes for Vc=10% of V0, we obtain
For 0.1V0
Rearrange terms
Solve for t
The RC time
What is the RC time of this circuit?

## Slide 22: Application of RC Circuits
What do you think the charging and discharging characteristics of RC circuits can be used for?
  To produce voltage pulses at a regular frequency
  How?
    The capacitor charges up to a particular voltage and discharges
    A simple way of doing this is to use breakdown of voltage in a gas filled tube
      The discharge occurs when the voltage breaks down at V0
      After the completion of discharge, the tube no longer conducts
      Then the voltage is at V0’ and it starts charging up
      How do you think the voltage as a function of time look?
        A sawtooth shape
    Pace maker, intermittent windshield wiper, etc

## Slide 23: Magnetism
What are magnets?
  Objects with two poles, north and south poles
    The pole that points to geographical north is the north pole and the other is the south pole
      Principle of compass
  These are called magnets due to the name of the region, Magnesia, where rocks that attract each other were found
What happens when two magnets are brought to each other?
  They exert force onto each other
  What kind?
  Both repulsive and attractive forces depending on the configurations
    Like poles repel each other while the unlike poles attract

## Slide 24: Magnetism
So the magnet poles are the same as the electric charge?
  No. Why not?
  While the electric charges (positive and negative) can be isolated the magnet poles cannot be isolated.
  So what happens when a magnet is cut?
    If a magnet is cut, two magnets are made.
    The more they get cut, the more magnets are made
  Single pole magnets are called the monopole but it has not been seen yet
Ferromagnetic materials: Materials that show strong magnetic effects
  Iron, cobalt, nickel, gadolinium and certain alloys
Other materials show very weak magnetic effects

## Slide 25: Magnetic Field
  The direction of the magnetic field is tangent to a line at any point
  The direction of the field is the direction the north pole of a compass would point to
  The number of lines per unit area is proportional to the strength of the magnetic field
  Magnetic field lines continue inside the magnet
  Since magnets always have both the poles, magnetic field lines form closed loops unlike electric field lines
Just like the electric field that surrounds electric charge, a magnetic field surrounds a magnet
What does this mean?
  Magnetic force is also a field force
  The force one magnet exerts onto another can be viewed as the interaction between the magnet and the magnetic field produced by the other magnet
  What kind of quantity is the magnetic field? Vector or Scalar?
So one can draw magnetic field lines, too.
Vector