## Slide 1: PHYS 1441 – Section 001 Lecture #10
Tuesday, June 21, 2016
Dr. Jaehoon Yu
Chapter 25
  Electric Current and Resistance
  The Battery
  Ohm’s Law: Resisters, Resistivity
  Electric Power
  Alternating Current
  Microscopic View of Electric Current
  Ohm’s Law in Microscopic View
  EMF and Terminal Voltage

## Slide 2: Announcements
Mid Term Exam
  In class tomorrow, Wednesday, June 22
  Covers CH21.1 through what we cover in class today + appendix
  Bring your calculator but DO NOT input formula into it!
    Cell phones or any types of computers cannot replace a calculator!
  BYOF: You may bring a one 8.5x11.5 sheet (front and back) of handwritten formulae and values of constants for the quiz
  No derivations, word definitions or solutions of any problems!
  No additional formulae or values of constants will be provided!
Reading assignments
  CH25. 8 – 25.10
Quiz 2 results
  Class average: 31.5/70
    Equivalent to 45/100
    Previous results: 48/100
  Top score: 59/70

## Slide 3: Electric Current and Resistance
So far we have been studying static electricity
  What is the static electricity?
    The charges so far has not been moving but staying put at the location they are placed.
Now we will learn dynamics of electricity
What is the electric current?
  A flow of electric charge
  A few examples of the things that use electric current in everyday lives?
In an electrostatic situation, there is no electric field inside a conductor but when there is current, there is field inside a conductor. Why?
  Electric field is needed to keep charges moving

## Slide 4: The Electric Battery
What is a battery?
  A device that produces electrical energy from the stored chemical energy and produces electricity  Maintains potential difference!
Electric battery was invented by Volta in 1790s in Italy
  It was made of disks of zinc and silver based on his research that certain combinations of materials produce a greater electromotive force (emf), or potential, than others
Simplest batteries contain two plates made of dissimilar metals called electrodes
  Electrodes are immersed in a solution, the electrolyte
  This unit is called a cell and many of these form a battery
Zinc and Iron in the figure are called terminals

## Slide 5: How does a battery work?
One of the electrodes in the figure is zinc and the other carbon
The acid electrolyte reacts with the zinc electrode and dissolves it.
Each zinc atom leaves two electrons in the electrode and enters into the solution as a positive ion  zinc electrode acquires negative charge and the electrolyte becomes positively charged
The carbon electrode picks up the positive charge
Since the two terminals are oppositely charged, there is a potential difference between them

## Slide 6: How does a battery work?
When the terminals are not connected, only the necessary amount of zinc is dissolved into the solution.
How is a particular potential maintained?
  As too many of zinc ion gets produced, if the terminals are not connected,
    zinc electrode gets increasingly charged up negative
    zinc ions get recombined with the electrons in zinc electrode
Why does battery go dead?
  When the terminals are connected, the negative charges will flow away from the zinc electrode
  More zinc atoms dissolve into the electrolyte to produce more charge
  One or more electrode get used up not producing any more charge.

## Slide 7: Electric Current
When a circuit is powered by a battery (or a source of emf) the charge can flow through the circuit.
Electric Current: Any flow of charge
  Current can flow whenever there is a potential difference between the ends of a conductor (or when the two ends have opposite charges)
    The current can flow even through the empty space under certain conditions
  Electric current in a wire can be defined as the net amount of charge that passes through the wire’s full cross section at any point per unit time (just like the flow of water through a conduit.)
  Average current is defined as:
  The instantaneous current is:
  What kind of a quantity is the current?
Unit of the current?
C/s
1A=1C/s
In a single circuit, conservation of electric charge guarantees that the current at one point of the circuit is the same as any other points on the circuit.
Scalar

## Slide 8: Example 25 – 1
Current is a flow of charge: A steady current of 2.5A flows in a wire for 4.0min. (a) How much charge passed by any point in the circuit? (b) How many electrons would this be?
Current is total amount charge flow through a circuit in a given time. So from we obtain
The total number of electrons passed through the circuit is

## Slide 9: Direction of the Electric Current
What do conductors have in abundance?
  Free electrons
What happens if a continuous loop of conducting wire is connected to the terminals of a battery?
  Electrons start flowing through the wire continuously as soon as both the terminals are connected to the wire. How?
    The potential difference between the battery terminals sets up an electric field inside the wire and in the direction parallel to it
    Free electrons in the conducting wire get attracted to the positive terminal
    The electrons leaving negative terminal flow through the wire and arrive at the positive terminal
      Electrons flow from negative to positive terminal
  Due to historical convention, the direction of the current is opposite to the direction of flow of electrons  Conventional Current

## Slide 10: Ohm’s Law: Resistance and Resistors
What do we need to produce electric current?
  Potential difference
Georg S. Ohm experimentally established that the current is proportional to the potential difference ( )
  If we connect a wire to a 12V battery, the current flowing through the wire is twice that of 6V, three times that of 4V and four times that of 3V battery.
  What happens if we reverse the sign of the voltage?
    It changes the direction of the current flow
    Does not change the magnitude of the current
  Just as in water flow case, if the height difference is large the flow rate is large  If the potential difference is large, the current is large.

## Slide 11: Ohm’s Law: Resistance
The exact amount of current flow in a wire depends on
  The voltage
  The resistance of the wire to the flow of electrons
    Just like the gunk in water pipe slows down water flow
    Electrons are slowed down due to interactions with the atoms of the wire
The higher the resistance the less the current for the given potential difference V
  So how would you define resistance?
    So that current is inversely proportional to the resistance
  Often it is rewritten as
  What does this mean?
    The metal conductor’s resistance R is a constant independent of V.
  This linear relationship is not valid for some materials like diodes, vacuum tubes, transistors etc.  These are called non-ohmic
Ohm’s Law
Unit?
ohms

## Slide 12: Example 25 – 4
Flashlight bulb resistance: A small flashlight bulb draws 300mA from its 1.5V battery. (a) What is the resistance of the bulb? (b) If the voltage drops to 1.2V, how would the current change?
From Ohm’s law, we obtain
If the resistance did not change, the current is
Would the current increase or decrease, if the voltage reduces to 1.2V?

## Slide 13: Ohm’s Law: Resistors
All electric devices offer resistance to the flow of current.
  Filaments of light bulbs or heaters are wires with high resistance to cause electrons to lose their energy in the wire
  In general connecting wires have low resistance compared to other devices on the circuit
In circuits, resistors are used to control the amount of current
  Resistors offer resistance of less than one ohm to millions of ohms
  Main types are
    “wire-wound” resistors which consists of a coil of fine wire
    “composition” resistors which are usually made of semiconductor carbon
    thin metal films
When drawn in the circuit, the symbol for a resistor is:
Wires are drawn simply as straight lines

## Slide 14: Ohm’s Law: Resistor Values
Resistors have its resistance color-coded on its body
The color-coding follows the convention below:
Color | Number | Multiplier | Tolerance
Black | 0 | 1=100 | 
Brown | 1 | 101 | 
Red | 2 | 102 | 
Orange | 3 | 103 | 
Yellow | 4 | 104 | 
Green | 5 | 105 | 
Blue | 6 | 106 | 
Violet | 7 | 107 | 
Gray | 8 | 108 | 
White | 9 | 109 | 
Gold |  | 10-1 | 5%
Silver |  | 10-2 | 10%
None |  |  | 20%
What is the resistance of the resistor in this figure?

## Slide 15: Resistivity
It is experimentally found that the resistance R of a metal wire is directly proportional to its length l and inversely proportional to its cross-sectional area A
  How would you formularize this?
  The proportionality constant ρ is called the resistivity and depends on the material used. What is the unit of this constant?
    ohm-m or Ω-m
    The values depends on purity, heat treatment, temperature, etc
  How would you interpret the resistivity?
    The higher the resistivity the higher the resistance
    The lower the resistivity the lower the resistance and the higher the conductivity  Silver has the lowest resistivity.
      So the silver is the best conductor
  The reciprocal of the resistivity is called the conductivity, σ,
A
l

## Slide 16: Example 25 – 5
Speaker wires: Suppose you want to connect your stereo to remote speakers. (a) If each wire must be 20m long, what diameter copper wire should you use to keep the resistance less than 0.1-Ω per wire? (b) If the current on each speaker is 4.0A, what is the voltage drop across each wire?
The resistivity of a copper is
From Ohm’s law, V=IR, we obtain
From the formula for resistance, we can obtain the formula for area
Solve for A
Solve for d
Table 25.1

## Slide 17: Example 25 – 6
Stretching changes resistance: A wire of resistance R is stretched uniformly until it is twice its original length. What happens to its resistance?
What is the constant quantity in this problem?
What is the volume of a cylinder of length L and radius r?
The volume!
What happens to A if L increases factor two, L’=2L?
The cross-sectional area, A, halves. A’=A/2
The original resistance is
The new resistance is
The resistance of the wire increases by a factor of four if the length increases twice.

## Slide 18: Temperature Dependence of Resistivity
Do you think the resistivity depends on temperature?
  Yes
Would it increase or decrease with the temperature?
  Increase
  Why?
  Because the atoms are vibrating more rapidly as temperature increases and are arranged in a less orderly fashion. So?
    They might interfere more with the flow of electrons.
If the temperature change is not too large, the resistivity of metals usually increase nearly linearly w/ temperature
  α is the temperature coefficient of resistivity
  α of some semiconductors can be negative due to increased number of freed electrons.

## Slide 19: Electric Power
Why is the electric energy useful?
  It can transform into different forms of energy easily.
    Motors, pumps, etc, transform electric energy to mechanical energy
    Heaters, dryers, cook-tops, etc, transforms electricity to thermal energy
    Light bulb filament transforms electric energy to light energy
      Only about 10% of the energy turns to light and the 90% lost via heat
      Typical household light bulb and heating elements have resistance of order a few ohms to a few hundred ohms
How does electric energy transforms to thermal energy?
  Flowing electrons collide with the vibrating atoms of the wire.
  In each collision, part of electron’s kinetic energy is transferred to the atom it collides with.
  The kinetic energy of wire’s atoms increases, and thus the temperature of the wire increases.
  The increased thermal energy can be transferred as heat through conduction and convection to the air in a heater or to food on a pan, through radiation to bread in a toaster or radiated as light.

## Slide 20: Electric Power
How do we find out the power transformed by an electric device?
  What is definition of the power?
    The rate at which work is done or the energy is transformed
What is the energy transformed when an infinitesimal charge dq moves through a potential difference V?
  dU=Vdq
  If dt is the time required for an amount of charge dq to move through the potential difference V, the power P is
  Thus, we obtain .
  What is the unit?
  What kind of quantity is the electrical power?
    Scalar
  P=IV can apply to any devices while the formula with resistance can only apply to devices that has resistance.
What is this?
Watts = J/s
In terms of resistance

## Slide 21: Example 25 – 8
Headlights: Calculate the resistance of a 40-W automobile headlight designed for 12V.
Since the power is 40W and the voltage is 12V, we use the formula with V and R.
Solve for R

## Slide 22: Power in Household Circuits
Household devices usually have small resistance
  But since they draw current, if they become large enough, wires can heat up (overloaded)
    Why is using thicker wires safer?
      Thicker wires has less resistance, lower heat
  Overloaded wire can set off a fire at home
How do we prevent this?
  Put in a switch that would disconnect the circuit when overloaded
    Fuse or circuit breakers
    They open up the circuit when the current is over certain value
Overload

## Slide 23: Example 25 – 11
Will a fuse blow?: Determine the total current drawn by all the devices in the circuit in the figure.
The total current is the sum of current drawn by individual device.
Solve for I
Bulb
Heater
Stereo
Dryer
Total current
What is the total power?

## Slide 24: Alternating Current
Does the direction of the flow of current change while a battery is connected to a circuit?
  No. Why?
    Because its source of potential difference stays put.
  This kind of current is called the Direct Current (DC), and it does not change its direction of flow while the battery is connected.
    How would DC look as a function of time?
      A straight line
Electric generators at electric power plant produce alternating current (AC)
  AC reverses direction many times a second
  AC is sinusoidal as a function of time
Most the currents supplied to homes and business are AC.

## Slide 25: The Alternating Current
The voltage produced by an AC electric generator is sinusoidal
  This is why the current is sinusoidal
Voltage produced can be written as
What are the maximum and minimum voltages?
  V0 (–V0) and 0
  The potential oscillates between +V0 and –V0, the peak voltages or amplitude
  What is f?
    The frequency, the number of complete oscillations made per second. What is the unit of f? What is the normal size of f in the US?
      f=60Hz in the US and Canada.
      Many European countries have f=50Hz.
  ω=2πf

## Slide 26: Alternating Current
Since V=IR, if a voltage V exists across a resistance R, the current I is
What are the maximum and minimum currents?
  I0 (–I0) and 0.
  The current oscillates between +I0 and –I0, the peak currents or amplitude. The current is positive when electron flows to one direction and negative when they flow opposite.
  AC is as many times positive as negative. What’s the average current?
    Zero. So there is no power and no heat is produced in a heater?
      Yes there is! The electrons actually flow back and forth, so power is delivered.
What is this?

## Slide 27: Power Delivered by Alternating Current
AC power delivered to a resistance is:
  Since the current is squared, the power is always positive
The average power delivered is
Since the power is also P=V2/R, we can obtain
The average of the square of current and voltage are important in calculating power:
Average power

## Slide 28: Power Delivered by Alternating Current
The square root of each of these are called root-mean-square, or rms:
rms values are sometimes called effective values
  These are useful quantities since they can substitute current and voltage directly in power, as if they are in DC
  In other words, an AC of peak voltage V0 or peak current I0 produces as much power as DC voltage of Vrms or DC current Irms.
  So normally, rms values in AC are specified or measured.
    US uses 115V rms voltage. What is the peak voltage?
    Europe uses 240V

## Slide 29: Example 25 – 13
Hair Dryer. (a) Calculate the resistance and the peak current in a 1000-W hair dryer connected to a 120-V AC line. (b) What happens if it is connected to a 240-V line in Britain?
The rms current is:
(b) If connected to 240V in Britain …
Thus the resistance is:
The peak current is:
The average power provide by the AC in UK is
So?
The heating coils in the dryer will melt!

## Slide 30: Microscopic View of Electric Current
When a potential difference is applied to the two ends of a wire w/ uniform cross-section, the direction of electric field is parallel to the walls of the wire, this is possible since the charges are moving
Let’s define a microscopic vector quantity, the current density, j, the electric current per unit cross-sectional area
  j=I/A or I = jA if the current density is uniform
  If not uniform
  The direction of j is the direction the positive charge would move when placed at that position, generally the same as E
The current density exists on any point in space while the current I refers to a conductor as a whole so a macroscopic

## Slide 31: Microscopic View of Electric Current
The direction of j is the direction of a positive charge. So in a conductor, since negatively charged electrons move, the direction is –j.
Let’s think about the current in a microscopic view again:
  When voltage is applied to the end of a wire
  Electric field is generated by the potential difference
  Electrons feel force and get accelerated
  Electrons soon reach to a steady average speed due to collisions with atoms in the wire, called drift velocity, vd
  The drift velocity is normally much smaller than electrons’ average random speed.

## Slide 32: Microscopic View of Electric Current
How do we relate vd with the macroscopic current I?
  In time interval Δt, the electrons travel l =vdΔt on average
  If wire’s x-sectional area is A, in time Δt electrons in a volume V=l A=AvdΔt will pass through the area A
  If there are n free electrons ( of charge –e) per unit volume, the total charge ΔQ that pass through A in time Δt is
  The current I in the wire is
  The density in vector form is
  For any types of charge:

## Slide 33: Microscopic View of Electric Current
The drift velocity of electrons in a wire is only about 0.05mm/s. How could we get light turned on immediately then?
  While the electrons in a wire travels slow, the electric field travels essentially at the speed of light. Then what is all the talk about electrons flowing through?
    It is just like water. When you turn on the facet, water flows right off the facet despite the fact that the water travels slow.
    Electricity is the same. Electrons fill the conductor wire and when the switch is flipped on or a potential difference is applied, the electrons closed to the positive terminal flows into the bulb.
    Interesting, isn’t it? Why is the field travel at the speed of light then?

## Slide 34: Ohm’s Law in Microscopic View
Ohm’s law can be written in microscopic quantities.
  Resistance in terms of resistivity is
  We can rewrite the potential V and current I as: I=jA, V=El.
  If electric field is uniform, from V=IR, we obtain
  So
  In a metal conductor, ρ or σ does not depend on V, thus, the current density j is proportional to the electric field E  Microscopic statement of Ohm’s Law
  In vector form, the density can be written as

## Slide 35: Superconductivity
At the temperature near absolute 0K, resistivity of certain material becomes 0.
  This state is called the “superconducting” state.
  Observed in 1911 by H. K. Onnes when he cooled mercury to 4.2K (-269oC).
    Resistance of mercury suddenly dropped to 0.
  In general superconducting materials become superconducting below a transition temperature.
  The highest temperature superconductivity seen is 160K
    First observation above the boiling temperature of liquid nitrogen is in 1987 at 90k observed from a compound of yttrium, barium, copper and oxygen.
Since much smaller amount of material can carry just as much current more efficiently, superconductivity can make electric cars more practical, computers faster, and capacitors store higher energy

## Slide 36: Electric Hazards: Leakage Currents
How does one feel shock by electricity?
  Electric current stimulates nerves and muscles, and we feel a shock
  The severity of the shock depends on the amount of current, how long it acts and through what part of the body it passes
  Electric current heats tissues and can cause burns
Currents above 70mA on a torso for a second or more is fatal, causing heart to function irregularly, “ventricular fibrillation”
A dry human body between two points on opposite side of the body is about 104 to 106 W.
When wet, it could be 103W.
A person in good contact with the ground who touches 120V DC line with wet hands can get the current:
  Could be lethal