## Slide 1: PHYS 1444 – Section 001 Lecture #11
Thursday, June 20, 2019
Dr. Jaehoon Yu
Chapter 25
  Electric Power
  Alternating Current
  Microscopic View of Electric Current
  Ohm’s Law in Microscopic View
  EMF and Terminal Voltage

## Slide 2: Nobel Meeting Photos
Good job for asking most the questions, class!

## Slide 3: Announcements
Quiz #3
  Beginning of the class Monday, June 24
  Covers CH25.1 through what we learn today
  BYOF: You may bring one 8.5x11.5 sheet (front and back) of handwritten formulae and values of constants for the exam
  No derivations, word definitions, setups or solutions of any problems!
  No additional formulae or values of constants will be provided!
We will have a mid-term grade discussion today, Thursday, June 20. We will have a class till 11:30am, followed by the discussion in my office (CPB342).
  Last name A – K:11:30 – 12:00
  Last name L – Y: 12:00 – 12:30

## Slide 4: Special Project #4
Make a list of the power consumption and the resistance of all electric and electronic devices at your home and compile them in a table. (10 points total for the first 10 items and 0.5 points each additional item.)
Estimate the cost of electricity for each of the items on the table using your own electric cost per kWh (if you don’t find your own, use $0.12/kWh) and put them in the relevant column. (5 points total for the first 10 items and 0.2 points each additional items)
Estimate the the total amount of energy in Joules and the total electricity cost per day, per month and per year for your home. (8 points)
Due: Beginning of the class Thursday, June 27

## Slide 6: Power in Household Circuits
Household devices usually have small resistance
  But since they draw current, if they become large enough, wires can heat up (overloaded)
    Why is using thicker wires safer?
      Thicker wires has less resistance, lower heat
  Overloaded wire can set off a fire at home
How do we prevent this?
  Put in a switch that would disconnect the circuit when overloaded
    Fuse or circuit breakers
    They open up the circuit when the current is over certain value
Overload

## Slide 7: Example 25 – 11
Will a fuse blow?: Determine the total current drawn by all the devices in the circuit in the figure.
The total current is the sum of current drawn by individual device.
Solve for I
Bulb
Heater
Stereo
Dryer
Total current
What is the total power?

## Slide 8: Alternating Current
Does the direction of the flow of current change while a battery is connected to a circuit?
  No. Why?
    Because its source of potential difference stays put.
  This kind of current is called the Direct Current (DC), and it does not change its direction of flow while the battery is connected.
    How would DC look as a function of time?
      A straight line
Electric generators at electric power plant produce alternating current (AC)
  AC reverses direction many times a second
  AC is sinusoidal as a function of time
Most the currents supplied to homes and business are AC.

## Slide 9: The Alternating Current
The voltage produced by an AC electric generator is sinusoidal
  This is why the current is sinusoidal
Voltage produced can be written as
What are the maximum and minimum voltages?
  V0 (–V0) and 0
  The potential oscillates between +V0 and –V0, the peak voltages or amplitude
  What is f?
    The frequency, the number of complete oscillations made per second. What is the unit of f? What is the normal size of f in the US?
      f=60Hz in the US and Canada.
      Many European countries have f=50Hz.
  ω=2πf

## Slide 10: Alternating Current
Since V=IR, if a voltage V exists across a resistance R, the current I is
What are the maximum and minimum currents?
  I0 (–I0) and 0.
  The current oscillates between +I0 and –I0, the peak currents or amplitude. The current is positive when electron flows to one direction and negative when they flow opposite.
  AC is as many times positive as negative. What’s the average current?
    Zero. So there is no power and no heat is produced in a heater?
      Yes there is! The electrons actually flow back and forth, so power is delivered.
What is this?

## Slide 11: Power Delivered by Alternating Current
AC power delivered to a resistance is:
  Since the current is squared, the power is always positive
The average power delivered is
Since the power is also P=V2/R, we can obtain
The average of the square of current and voltage are important in calculating power:
Average power

## Slide 12: Power Delivered by Alternating Current
The square root of each of these are called root-mean-square, or rms:
rms values are sometimes called the effective values
  These are useful quantities since they can substitute current and voltage directly in power, as if they are in DC
  In other words, an AC of peak voltage V0 or peak current I0 produces as much power as DC voltage of Vrms or DC current Irms.
  So normally, rms values in AC are specified or measured.
    US uses 115V rms voltage. What is the peak voltage?
    Europe uses 240V

## Slide 13: Example 25 – 13
Hair Dryer. (a) Calculate the resistance and the peak current in a 1000-W hair dryer connected to a 120-V AC line. (b) What happens if it is connected to a 240-V line in Britain?
The rms current is:
(b) If connected to 240V in Britain …
Thus the resistance is:
The peak current is:
The average power provide by the AC in UK is
So?
The heating coils in the dryer will melt!