## Slide 1: PHYS 1444 – Section 001 Lecture #13
Tuesday, June 25, 2019
Dr. Jaehoon Yu
Chapter 26
  Kirchhoff’s Rules
  EMFs in Series and Parallel
  RC Circuits
Chapter 27: Magnetism and Magnetic Field
  Electric Current and Magnetism
  Magnetic Forces on Electric Current
  About Magnetic Field

## Slide 2: Announcements
2nd Term Exam
  First 80min this Wednesday, June 26, tomorrow
  Covers CH25.1 through what we learn today
  BYOF: You may bring one 8.5x11.5 sheet (front and back) of handwritten formulae and values of constants for the exam
  No derivations, word definitions, setups or solutions of any problems!
  No additional formulae or values of constants will be provided!
Quiz 3 results
  Class average: 40.7/60
    Equivalent to 67.8/100
    Previous quizzes: 44.3/100 and 54.2/100
  Top score: 60/60

## Slide 3: Reminder: Special Project #4
Make a list of the power consumption and the resistance of all electric and electronic devices at your home and compile them in a table. (10 points total for the first 10 items and 0.5 points each additional item.)
Estimate the cost of electricity for each of the items on the table using your own electric cost per kWh (if you don’t find your own, use $0.12/kWh) and put them in the relevant column. (5 points total for the first 10 items and 0.2 points each additional items)
Estimate the the total amount of energy in Joules and the total electricity cost per day, per month and per year for your home. (8 points)
Due: Beginning of the class this Thursday, June 27

## Slide 5: Kirchhoff’s Rules – the 1st Rule
Some circuits are very complicated to do the analysis using the simple combinations of resistors
  G. R. Kirchhoff devised two rules to deal with complicated circuits.
Kirchhoff’s rules are based on conservation of charge and energy
  Kirchhoff’s 1st rule: The junction rule, charge conservation.
    At any junction point, the sum of all currents entering the junction must equal to the sum of all currents leaving the junction.
    In other words, what goes in must come out.
    At junction a in the figure, I3 comes into the junction while I1 and I2 leaves: I3 = I1+ I2

## Slide 6: Kirchhoff’s Rules – the 2nd Rule
Kirchoff’s 2nd rule: The loop rule, uses conservation of energy.
  The sum of the changes in potential in any closed path of a circuit must be zero.
The current in the circuit in the figure is I=12/690=0.017A.
  Point e is the high potential point while point d is the lowest potential.
  When the test charge starts at e and returns to e, the total potential change is 0.
  Between point e and a, no potential change since there is no source of potential nor any resistance.
  Between a and b, there is a 400Ω resistance, causing IR=0.017*400 =6.8V drop.
  Between b and c, there is a 290Ω resistance, causing IR=0.017*290 =5.2V drop.
  Since these are voltage drops, we use negative sign for these, -6.8V and -5.2V.
  No change between c and d while from d to e there is +12V change.
  Thus the total change of the voltage through the loop is: -6.8V-5.2V+12V=0V.

## Slide 7: Using Kirchhoff’s Rules
Determine the flow of currents at the junctions and label each and everyone of the currents.
  It does not matter which direction, you decide but keep it!
  If the value of the current after completing the calculations are negative, you just need to flip the direction of the current flow.
Write down the current equation based on Kirchhoff’s 1st rule at various junctions.
  Be sure to see if any of equations are the same.
Choose closed loops in the circuit
Write down the potential in each interval of the junctions, keeping the sign properly.
Write down the potential equations for each loop.
Solve the equations for unknowns.

## Slide 8: Example 26 – 9
Use Kirchhoff’s rules. Calculate the currents I1, I2 and I3 in each of the branches of the circuit in the figure.
The directions of the current through the circuit is not known a priori but since the current tends to move away from the positive terminal of a battery, we arbitrarily choose the direction of the currents as shown.
This is the same for junction d as well, so no additional information.
We have three unknowns so we need three equations.
Using Kirchhoff’s junction rule at point a, we obtain
Now the second rule on the loop ahdcba.
The total voltage change in the loop ahdcba is.

## Slide 9: Example 26 – 9, cnt’d
So the three equations become
Now the second rule on the other loop agfedcba.
The total voltage change in loop agfedcba is.
We can obtain the three current by solving these equations for I1, I2 and I3.
Do this yourselves!!

## Slide 10: EMFs in Series and Parallel: Charging a Battery
When two or more sources of emfs, such as batteries, are connected in series
  The total voltage is the algebraic sum of their voltages, if their direction is the same
    Vab=1.5 + 1.5=3.0V in figure (a).
  If the batteries are arranged in the opposite direction, the total voltage is the difference between them
    Vac=20 – 12=8.0V in figure (b)
    Connecting batteries in opposite direction is wasteful.
    This, however, is the way a battery charger works.
    Since the 20V battery is at a higher voltage, it forces charges into 12V battery
    Some battery are rechargeable since their chemical reactions are reversible but most the batteries do not reverse their chemical reactions
Parallel arrangements (c) are used only to increase currents. An example?

## Slide 11: RC Circuits
Circuits containing both resistors and capacitors
  RC circuits are used commonly in everyday life
    Control windshield wiper
    Timing of traffic light from red to green
    Camera flashes and heart pacemakers
How does an RC circuit look?
  There should be a source of emf, capacitors and resisters
What happens when the switch S is closed?
  Current immediately starts flowing through the circuit.
  Electrons flow out of negative terminal of the emf source, through the resister R and accumulates on the upper plate of the capacitor.
  The electrons from the bottom plate of the capacitor will flow into the positive terminal of the battery, leaving only the positive charge on the bottom plate.
  As the charge accumulates on the capacitor, the potential difference across it increases
  The current reduces gradually to 0 till the voltage across the capacitor is the same as the emf.
  The charge on the capacitor increases till it reaches to its maximum CE.

## Slide 12: RC Circuits
How does all this look like in graphs?
  The charge and the current on the capacitor as a function of time
  From energy conservation (Kirchhoff’s 2nd rule), the emf E must be equal to the sum of voltage drop across the capacitor and the resister
    E=IR+Q/C
    R includes all resistance in the circuit, including the internal resistance of the battery, I is the current in the circuit at any instance, and Q is the charge of the capacitor at that same instance.

## Slide 13: Analysis of RC Circuits
In an RC circuit and
What can we see from the above equations?
  Q and VC increase from 0 at t=0 to maximum value Qmax=CE and VC= E.
In how much time?
  The quantity RC is called the time constant of the circuit, τ
    τ=RC, What is the unit?
  What is the physical meaning?
    The time required for the capacitor to reach (1 - e-1)=0.63 or 63% of the full charge
The current is
Sec.

## Slide 14: Example 26 – 12
RC circuit, with emf. The capacitance in the circuit of the figure is C=0.30μF, the total resistance is 20kΩ, and the battery emf is 12V. Determine (a) the time constant, (b) the maximum charge the capacitor could acquire, (c) the time it takes for the charge to reach 99% of this value, (d) the current I when the charge Q is half its maximum value, (e) the maximum current, and (f) the charge Q when, the current I is 0.20 its maximum value.
(a) Since
We obtain
(c) Since
The current when Q is 0.5Qmax
(b) Maximum charge is
For 99% we obtain
(d) Since
We obtain
(e) When is I maximum?
when Q=0:
(f) What is Q when I=120mA?

## Slide 15: Discharging RC Circuits
  The rate at which the charge leaves the capacitor equals the negative of the current flows through the resistor
    I= - dQ/dt
    This is because the current is leaving the capacitor
  Thus the voltage equation becomes a differential equation
When a capacitor is already charged, it is allowed to discharge through a resistance R.
  When the switch S is closed, the voltage across the resistor at any instant equals that across the capacitor. Thus IR=Q/C.
Rearrange terms

## Slide 16: Discharging RC Circuits
  Now, let’s integrate from t=0 when the charge is Q0 to t when the charge is Q
  The result is
  Thus, we obtain
  What does this tell you about the charge on the capacitor?
    It decreases exponentially w/ time at the time constant RC
    Just like the case of charging
  The current is:
    The current also decreases exponentially w/ time w/ the time constant RC
What is this?

## Slide 17: Example 26 – 13
Discharging RC circuit. In the RC circuit shown in the figure the battery has fully charged the capacitor, so Q0=CE. Then at t=0, the switch is thrown from position a to b. The battery emf is 20.0V, and the capacitance C=1.02μF. The current I is observed to decrease to
(a) Since the current reaches to 0.5 of its initial value in 40μs, we can obtain
(b) The value of Q at t=0 is
0.50 of its initial value in 40μs. (a) what is the value of R? (b) What is the value of Q, the charge on the capacitor, at t=0? (c) What is Q at t=60μs?
For 0.5I0
Rearrange terms
Solve for R
The RC time
(c) What do we need to know first for the value of Q at t=60μs?
Thus

## Slide 18: Application of RC Circuits
What do you think the charging and discharging characteristics of RC circuits can be used for?
  To produce voltage pulses at a regular frequency
  How?
    The capacitor charges up to a particular voltage and discharges
    A simple way of doing this is to use breakdown of voltage in a gas filled tube
      The discharge occurs when the voltage breaks down at V0
      After the completion of discharge, the tube no longer conducts
      Then the voltage is at V0’ and it starts charging up
      How do you think the voltage as a function of time look?
        A sawtooth shape
    Pace maker, intermittent windshield wiper, etc

## Slide 19: Magnetism
What are magnets?
  Objects with two poles, North and South poles
    The pole that points to the geographical North is the North pole and the other is the South pole
      Principle of compass
  These are called the magnet due to the name of the region, Magnesia, where the rocks that attract each other were found
What happens when two magnets are brought to each other?
  They exert force onto each other
  What kind?
  Both repulsive and attractive forces depending on the configurations
    Like poles repel each other while the unlike poles attract

## Slide 20: Magnetism
So the magnetic poles are the same as the electric charge?
  No. Why not?
  While the electric charges (positive and negative) can be isolated, the magnetic poles cannot be isolated.
  So what happens when a magnet is cut?
    If a magnet is cut, two magnets are made.
    The more they get cut, the more magnets are made
  Single pole magnets are called the monopole but it has not been seen yet
Ferromagnetic materials: Materials that show strong magnetic effects
  Iron, cobalt, nickel, gadolinium and certain alloys
Other materials show very weak magnetic effects

## Slide 21: Magnetic Field
  The direction of the magnetic field is tangential to the field line at any point
  The direction of the field is the direction the north pole of a compass would point to; out of N and into S
  The number of lines per unit area is proportional to the strength of the magnetic field
  Magnetic field lines continue inside the magnet
  Since magnets always have both the poles, magnetic field lines form closed loops unlike electric field lines
Just like the electric field that surrounds electric charge, a magnetic field surrounds a magnet
What does this mean?
  Magnetic force is also a field force
  The force one magnet exerts onto another can be viewed as the interaction between the magnet and the magnetic field produced by the other magnet
  What kind of quantity is the magnetic field? Vector or Scalar?
So one can draw magnetic field lines, too.
Vector

## Slide 22: Earth’s Magnetic Field
What magnetic pole does the geographic North pole has to have?
  Magnetic South pole. What? How do you know that?
  Since the magnetic North pole points to the geographic North, the geographic north must have magnetic south pole
    The pole in the North is still called geomagnetic North pole just because it is in the North
  Similarly, South pole has magnetic North pole
The Earth’s magnetic poles do not coincide with the geographic poles  magnetic declination
  Geomagnetic North pole is in Northern Canada, some 900km off the true North pole
Earth’s magnetic field line is not tangent to the earth’s surface at all points
  The angle the Earth’s field makes to the horizontal line is called the angle dip

## Slide 23: Electric Current and Magnetism
In 1820, Oersted found that when a compass needle is placed near an electric wire, the needle deflects as soon as the wire is connected to a battery and the current flows
  Electric current produces a magnetic field
    The first indication that electricity and magnetism are of the same origin
  What about a stationary electric charge and magnet?
    They don’t affect each other.
The magnetic field lines produced by a current in a straight wire is in the form of circles following the “right-hand” rule
  The field lines follow right-hand fingers wrapped around the wire when the thumb points to the direction of the electric current

## Slide 24: Directions in a Circular Wire?
OK, then what is the direction of the magnetic field generated by the current flowing through a circular loop?

## Slide 25: Magnetic Forces on Electric Current
Since the electric current exerts force on a magnet, the magnet should also exert force on the electric current
  Which law justifies this?
    Newton’s 3rd law
  This was also discovered by Oersted
Direction of the force is always
  perpendicular to the direction of the current
  perpendicular to the direction of the magnetic field, B
Experimentally the direction of the force is given by another right-hand rule  When the fingers of the right-hand points to the direction of the current and the finger tips bent to the direction of magnetic field B, the direction of thumb points to the direction of the force

## Slide 26: Magnetic Forces on Electric Current
OK, we are set for the direction but what about the magnitude?
It is found that the magnitude of the force is directly proportional
  To the current in the wire
  To the length of the wire in the magnetic field (if the field is uniform)
  To the strength of the magnetic field
The force also depends on the angle θ between the directions of the current and the magnetic field
  When the wire is perpendicular to the field, the force is the strongest
  When the wire is parallel to the field, there is no force at all
Thus the force on current I in the wire w/ length l in a uniform field B is