## Slide 1: PHYS 1441 – Section 001 Lecture #18
Tuesday, July 7, 2020
Dr. Jaehoon Yu
CH 29:EM Induction & Faraday’s Law
  Induced EMF and EM Induction
  Faraday’s Law of Induction
  Lenz’s Law
  Generation of Electricity
  Transformer and Transformer Equation
Chapter 30: Inductance
  Mutual and Self Inductance

## Slide 2: Announcements
Reading Assignments: CH28.6 – 10
Course feedback survey  Check the course evaluation tab in Canvas
Further questions on COVID–19 to Dr. Linda Lee (lindalee.17@gmail.com)
Online Final Exam in the class Thursday, July 9 (roll call at 10:20am)
  Covers CH21.1 to what we finish this Wednesday plus the math refresher
  BYOF You may bring a one 8.5x11.5 sheet (front and back) of handwritten formulae and values of constants for the exam
  No derivations, word definitions, figures, pictures, arrows, or setups or solutions of any problems!
  No additional formulae or values of constants will be provided!
  Must send me the photos of front and back of the formula sheet, including the blank, no later than 10am Thursday!
    Once submitted, you cannot change, unless I ask you to delete some part of the sheet!

## Slide 3: Induced EMF
It has been discovered by Oersted and company in early 19th century that
  Magnetic field can be produced by the electric current
  Magnetic field can exert force on the electric charge
So if you were scientists at that time, what would you wonder?
  Yes, you are absolutely right! You would wonder if the magnetic field can create the electric current.
  An American scientist Joseph Henry and an English scientist Michael Faraday independently found that it was possible
    Faraday was given the credit since he published his work before Henry
      He also did a lot of detailed studies on magnetic induction

## Slide 4: Electromagnetic Induction
Faraday used an apparatus below to show that magnetic field can induce current
Despite his hope, he did not see steady current induced on the other side when the switch is thrown
But he did see that the needle on the Galvanometer turns strongly when the switch is initially thrown and is opened
  When the magnetic field through coil Y changes, a current flows as if there were a source of emf
Thus he concluded that an induced emf is produced by a changing magnetic field  Electromagnetic Induction

## Slide 5: Electromagnetic Induction
Further studies on electromagnetic induction taught
  If a magnet is moved quickly into a coil of wire, a current is induced in the wire in one direction
  If a magnet is removed from the coil, a current is induced in the wire in the opposite direction
  By the same token, the current can also be induced if the magnet stays put but the coil moves toward or away from the magnet
  Current is also induced if the coil rotates.
In other words, it does not matter whether the magnet or the coil moves. It is the relative motion that counts.

## Slide 6: Magnetic Flux
So what do you think is the induced emf proportional to?
  The rate of changes of the magnetic field?
    the higher the changes the higher the induction
  Not really, it rather depends on the rate of change of the magnetic flux, ΦB.
  Magnetic flux is defined as (just like the electric flux)
    θ is the angle between B and the area vector A whose direction is perpendicular to the face of the loop based on the right-hand rule
  What kind of quantity is the magnetic flux? (Poll 1)
    Scalar. Unit?
    or weber
If the area of the loop is not simple or B is not uniform, the magnetic flux can be written as

## Slide 7: Faraday’s Law of Induction
In terms of magnetic flux, we can formulate Faraday’s findings
  The emf induced in a circuit is equal to the rate of change of magnetic flux through the circuit
If the circuit contains N closely wrapped loops, the total induced emf is the sum of emf induced in each loop
  Why negative?
    Has got a lot to do with the direction of induced emf…
Faraday’s Law of Induction

## Slide 8: Lenz’s Law
It is experimentally found that
  An induced emf gives rise to the current whose magnetic field opposes the original change in flux  This is known as Lenz’s Law
  In other words, an induced emf is always in the direction that opposes the original change in flux that caused it.
  We can use Lenz’s law to explain the following cases in the figures
    When the magnet is moving into the coil
      Since the external flux increases, the field inside the coil takes the opposite direction to minimize the change and causes the current to flow clockwise
    When the magnet is moving out
      Since the external flux decreases, the field inside the coil takes the opposite direction to compensate the loss, causing the current to flow counter-clockwise
Which law is Lenz’s law result of?
  Energy conservation. Why?

## Slide 9: Induction of EMF
How can we induce emf?
Let’s look at the formula for the magnetic flux
What do you see? What are the things that can change with time to result in change of magnetic flux?
  Magnetic field
  The area of the loop
  The angle θ between the field and the area vector

## Slide 10: Example 29 – 5
Pulling a coil from a magnetic field. A square coil of wire with side 5.00cm contains 100 loops and is positioned perpendicular to a uniform 0.600-T magnetic field. It is quickly and uniformly pulled from the field (moving perpendicular to B) to a region where B drops abruptly to zero. At t=0, the right edge of the coil is at the edge of the field. It takes 0.100s for the whole coil to reach the field-free
What should be computed first?
The flux at t=0 is
The change of flux is
region. Find (a) the rate of change in flux through the coil, (b) the emf and the current induced, and (c) how much energy is dissipated in the coil if its resistance is 100Ω. (d) what was the average force required?
The initial flux at t=0.
Thus the rate of change of the flux is

## Slide 11: Example 29 – 5, cnt’d
Thus the total emf induced in this period is
Which direction would the induced current flow?
The total energy dissipated is
Force for each coil is
The induced current in this period is
Clockwise
Force for N coil is

## Slide 12: EMF Induced on a Moving Conductor
Another way of inducing emf is using a U shaped conductor with a movable rod resting on it.
As the rod moves at a speed v, it travels vdt in time dt, changing the area of the loop by dA=lvdt.
Using Faraday’s law, the induced emf for this loop is
  This equation is valid as long as B, l and v are perpendicular to each other. What do we do if not?
    Use the scalar product of vector quantities
An emf induced on a conductor moving in a magnetic field is called a motional emf

## Slide 13: Electric Generators
What does a generator do?
  Transforms mechanical energy into the electrical energy
  What does this look like?
    An inverse of an electric motor which transforms electrical energy to mechanical energy
  An electric generator is also called a dynamo
Whose law does the generator based on?
  Faraday’s law of induction

## Slide 14: How does an Electric Generator work?
An electric generator consists of
  Many coils of wires wound on an armature that can rotate by mechanical means in a magnetic field
An emf is induced in the rotating coil
Electric current is the output of a generator
Which direction does the output current flow when the armature rotates counterclockwise?
  The conventional current flows outward on wire A toward the brush
  After half the revolution the wire A will be where the wire C is and the current flow on A is reversed
Thus the current produced is alternating its direction

## Slide 15: How does an Electric Generator work?
Let’s assume the loop is rotating in a uniform B field w/ a constant angular velocity ω. The induced emf is
What is the variable that changes above?
  The angle θ. What is dθ/dt?
    The angular speed ω.
  So θ=θ0+ωt
  If we choose θ0=0, we obtain
  If the coil contains N loops:
  What is the shape of the output?
    Sinusoidal w/ the amplitude ε0=NBAω
USA frequency is 60Hz. Europe is at 50Hz
  Most the U.S. power is generated at steam plants

## Slide 16: Example 29 – 9
An AC generator. The armature of a 60-Hz AC generator rotates in a 0.15-T magnetic field. If the area of the coil is 2.0x10-2m2, how many loops must the coil contain if the peak output is to be ε0=170V?
The maximum emf of a generator is
Solving for N
Since
We obtain

## Slide 17: US Electricity Sources

## Slide 18: US Electric E Consumption by Users
US Energy Information Administration http://www.eia.gov/electricity/

## Slide 19: The World Energy Consumption
In 2016, total worldwide energy consumption was 567 EJ (567×1018 J=157 PWh) expected >1000EJ by 2050
  Equivalent to an average energy consumption rate of 18 terawatts (1.8×1013 W)
  US uses 39.1 PWh (1.38kWh/person, as of 2014)
The potential for renewable energy
  solar energy 1600 EJ (444,000 TWh)
  wind power 600 EJ (167,000 TWh)
  geothermal energy 500 EJ (139,000 TWh),
  biomass 250 EJ (70,000 TWh)
  hydropower 50 EJ (14,000 TWh) an
  ocean energy 1 EJ (280 TWh)
  Read this paper if you want to learn more

## Slide 20: A DC Generator
A DC generator is almost the same as an AC generator except the slip rings are replaced by split-ring commutators
Output can be smoothed out by placing a capacitor in parallel to the output
  More commonly done using many armature windings
Smooth output using many windings

## Slide 21: Transformer
What is a transformer?
  A device for increasing or decreasing an AC voltage
  A few examples?
    TV sets to provide the high voltage to picture tubes, portable electronic device converters, transformers on the pole, etc
A transformer consists of two coils of wires known as the primary and the secondary
  The two coils can be interwoven or linked by a laminated soft iron core to reduce losses due to Eddy current
Transformers are designed so that all magnetic flux produced by the primary coil pass through the secondary

## Slide 22: How does a transformer work?
When an AC voltage is applied to the primary, the changing B it produces will induce voltage of the same frequency in the secondary wire
So how would we make the voltage different?
  By varying the number of loops in each coil
  From Faraday’s law, the induced emf in the secondary is
  The input primary voltage is
  Since dΦB/dt is the same, we obtain
Transformer Equation

## Slide 23: Transformer Equation
The transformer equation does not work for DC current
  Since there is no change of magnetic flux!!
If NS>NP, the output voltage is greater than the input so it is called a step-up transformer while NS<NP is called step-down transformer
Now, it looks like energy conservation is violated since we can get more emf from smaller ones, right?
  Wrong! Wrong! Wrong! Energy is always conserved!
  A well designed transformer can be more than 99% efficient
  The power output is the same as the input:
The output current for a step-up transformer will be lower than the input, while it is larger for a step-down x-former than the input.

## Slide 24: Example for A Transformer
Portable radio transformer. A transformer for home use of a portable radio reduces 120-V AC to 9.0V AC. The secondary contains 30 turns, and the radio draws 400mA. Calculate (a) the number of turns in the primary (b) the current in the primary and (c) the power transformed.
(a) What kind of a transformer is this?
A step-down x-former
Since
We obtain
(b) Also from the transformer equation
We obtain
(c) Thus the power transformed is
How about the input power?
The same assuming 100% efficiency.

## Slide 25: Example 29 – 13: Power Transmission
Transmission lines. An average of 120kW of electric power is sent to a small town from a power plant 10km away. The transmission lines have a total resistance of 0.4Ω. Calculate the power loss if the power is transmitted at (a) 240V and (b) 24,000V.
We cannot use P=V2/R since we do not know the voltage along the transmission line. We, however, can use P=I2R.
(a) If 120kW is sent at 240V, the total current is
Thus the power loss due to transmission line is
(b) If 120kW is sent at 24,000V, the total current is
Thus the power loss due to transmission line is
The higher the transmission voltage, the smaller the current, causing less loss of energy. This is why power is transmitted w/ HV, as high as 170kV.